## Slide 1: Communication & Network Security
(CNS) Code: EC6112
Semeste: 6th
Branch:E&CSc

## Slide 2: Course Outcomes
Course Outcome: At the end of the course, the students will be able to :
CO1. Analyze different security threats and attacks with reference to ISO/OSI model security.
CO2. Differentiate between various cryptography, watermarking, steganography methods.
CO3. Analyze different Symmetric and Asymmetric cryptographic algorithms.
CO4. Differentiate various key distribution and Digital Signature.
CO5. Analyze the working of various communication security protocols with respect to OSI layer.
CO6. Analyze different network security systems implementation in Wireless systems.

## Slide 3: Syllabus
Prerequisite: Data Communication and Networking (EC 3028)
Introduction: Cryptography, Watermarking, Steganography, Escrow & Crypt Analysis, ISO/OSI reference model & security, Security threatening attacks & actions, Reviews of mathematical foundations (Logarithms, Prime Number, GCD, Groups, Rings, Fields, Fermat’s Theorem, Euler’s Theorem, Exclusive-Or, Random Numbers).
Ciphers &Algorithm: Symmetric Ciphers, Asymmetric Ciphers systems, Elliptic Curve Crypto systems, RSA A

## Slide 4: Syllabus
Cryptographic Key distribution system:Key Distribution, Merkle’s Puzzle Method, Shamir’s Key Distribution Method, Digital Signature.
Communication Security layer classification: A synergistic security frame work, Firewalls & Gateways, Security Cross- portfolios, attacks and security in the internet, TACACS.
Network security: Wireless system: WLAN security, IEEE 802.11i robust security network and vulnerabilities, GSM Security, B3G/4G Security Concerns, Wimax Security, and Communication Satellite network security, Wireless Adhoc Network Security.

## Slide 5: Text Books
Text Book
1. Cryptography & Network Security by B A Forouzan and D Mukhopadhyay, Mc-Graw Hill, India, 2ndEdition, 2010.
2. Security of Information and Communication Network by S V. Kartalopoulos, Wiley-IEEE Press., 2009.
Reference Book
1. Handbook of Information and Communication Security by Stavroulakis, Peter; Springer, 2010
2. Secure Broadcast communication in Wired and Wireless Communication. By Adrian Perrig& Doug Tygar, Kluwer Publication, 2002.
3. Modern Cryptography: Theory and Practice by W Mao, Pearson Education, India, 1st Edition, 2003.

## Slide 6: OSI Model and Layering

## Slide 7: OSI Model and Layering
We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.

## Slide 8: Tasks involved in sending a letter

## Slide 9: THE OSI MODEL
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
ISO is an organization.
(ISO:Internation Standard Organization)
OSI is a model.
(Open Systey )

## Slide 10: THE OSI MODEL

## Slide 11: The interaction between layers in the OSI model

## Slide 12: An exchange of data using the OSI model
Encapulation
Decapulation

## Slide 13: Physical Charecteresyics of OSI Model Layers

## Slide 14: Physical Charecteresyics of Physical Layer
Responsibilities:
Modulation
Line codind
Syncronization of bits
Interface
Topology
Transmission
The physical layer is responsible for movements of individual bits from one hop (node) to the next.

## Slide 15: Physical Charecteresyics of Data Link Layer
Responsibilities:
Framing
Physical Addressing (07:01:02:01:2C:4B (6-bytes))
Flow Control
Error Control
Access Control
The data link layer is responsible for moving frames from one hop (node) to the next.

## Slide 16: Physical Charecteresyics of Network Layer
Responsibilities:
Logical Addressing (IP addressing: IPV4 (192.172.10.2 (32-bit)) and IPV6 (AB12:23CD:45AC:123A:ACBD:1265 (128-bit))
Routing
The network layer is responsible for the delivery of individual packets from the source host to the destination host.

## Slide 17: Physical Charecteresyics of Transport Layer
Responsibilities:
Source addressing (Socket addressing= IP address + Port no)
Flow Control
Error Control
The transport layer is responsible for the delivery of a message from one process to another.

## Slide 18: Physical Charecteresyics of Session Layer
Responsibilities:
Dialogue control
Synchronisation
The session layer is responsible for dialog control and synchronization.

## Slide 19: Physical Charecteresyics of Presentation Layer
Responsibilities:
Translation
Encryption
Compression
The presentation layer is responsible for translation, compression, and encryption.

## Slide 20: Physical Charecteresyics of Application Layer
Responsibilities:
Providing services to the end usr
HTTP (Hypertext Transfer Protocol )
FTP (File Trasfer Protocol)
SMTP (Simple mail Transfer Protocol)
The application layer is responsible for providing services to the user.

## Slide 21: Summery of Layers

## Slide 22: TCP/IP PROTOCOL SUITE
The layers in the TCP/IP protocol suite do not exactly match those in the OSI model. The original TCP/IP protocol suite was defined as having four layers: host-to-network, internet, transport, and application. However, when TCP/IP is compared to OSI, we can say that the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.

## Slide 23: TCP/IP PROTOCOL SUITE

## Slide 24: Security Goals

## Slide 25: Confidentiality

## Slide 26: Integrity and Availability

## Slide 27: Security Attacks

## Slide 29
(Spoofing)

## Slide 30: Replaying and Repudiation

## Slide 32
Categorization of Passive Vs Active Attacks

## Slide 33
Passive and Active Attacks

## Slide 35: SECURITY SERVICES

## Slide 36: Data Confidentiality
Data confidentiality if designed to protect data from disclosure attack

## Slide 37: Data Integrity

## Slide 38: Authentication

## Slide 39: Nonrepudiation

## Slide 40: Access Control

## Slide 41: Security Mechanisms

## Slide 42: Encipgerment

## Slide 43: Data Integrity

## Slide 44: Digital Signature

## Slide 45: Authentication Exchange

## Slide 46: Traffic Padding

## Slide 47: Routing Control

## Slide 48: Notarization

## Slide 49: Access Control

## Slide 50: Reltion between Sevices and Mechanisms

## Slide 51: TECHNIQUES
The actual implementation of security goals need some techniques
Type of Tccniques:
CRYPTOGRAPHY
  Symmetric-Key Encipherment
  Asymmetric-Key Encipherment
  Hashing
STEGANOGRAPHY

## Slide 52: Cryptography

## Slide 53: Cryptography
Steganography means concealing the message itself by covering it with something else
Cryptography means concealing the contents of message by enciphering

## Slide 54: Symmetric-Key Encipherment

## Slide 55: What is Encryption/ Decryption

## Slide 56: Symmentric Cryptography

## Slide 57: Symmetric-key Encipherment
Alice
Bob

## Slide 58: Asymmetric Key Cryptography

## Slide 59: Asymmetric Key Encipherment

## Slide 60: Asymmetric-key Encipherment

## Slide 61: Cryptography (Encryption/Decryption)

## Slide 62: Cryptography

## Slide 63: Symmetric-key Encipherment
Alice
Bob

## Slide 64: Symmentric Cryptography

## Slide 65: Asymmetric-Key Encipherment

## Slide 67: Cryptography (Encryption/Decryption)

## Slide 68: What is Cryptography

## Slide 69: What is Encryption/ Decryption